Vi invio questa procedura visto che mi è stata richiesta da ("Sandro Bernero" <s.bernero@virgilio.it>)

Questa Procedura serve per utilizzare il router Atlantis A02-RA3+ con Emule con la possibilità di avere attivo anche il Firewall.

1 Connettetevi al router via http:(IP del router) ad esempio 192.168.0.254  (di default è 192.168.1.254)

2 Cliccate su Configuration

Status

Quick Start

Configuration

Save Config to FLASH

Language

Vi apparirà questo…

Status

Quick Start

Configuration

LAN

WAN

System

Firewall

VPN

QoS

Virtual Server

Advanced

Save Config to FLASH

Language

3 Cliccate su Firewall e vi troverete qua

Status

Quick Start

Configuration

LAN

WAN

System

Firewall

General Settings

Packet Filter

Intrusion Detection

MAC Address Filter

URL Filter

Firewall Log

VPN

QoS

Virtual Server

Advanced

Save Config to FLASH

Language

4 cliccate su General setting e impostate come nella figura sotto

| General Settings |
| --- |
| Firewall Security Inizio modulo |
| Security | Enable Disable |
| Policy | All blocked/User-defined |
|  | High security level |
|  | Medium security level |
|  | Low security level |
| (If some applications cannot work after enabling Firewall, please check the Packet Filter especially Port Filter rules. For example, adding (TCP:443,outbound allowed) will let HTTPS data go through Firewall.) |
| Block WAN Request | Enable Disable |
| (Enable for preventing any ping test from Internet, such as hacker attack.) |
| Fine modulo |

5 cliccate su Apply per rendere attivo il firewall.

6 Dopo avere attivato il firewall ritornate al punto 3 e cliccate su Firewall e poi su Packet filter in modo da trovarvi qua…

| Packet Filter |
| --- |
| Firewall Security |
| Type | Configuration | Note |
| external < > internal | Port Filters | Address Filters | 1. By default, all protocol types and TCP/UDP ports are blocked. 2. Only the listed IP addresses are blocked |

7 ora cliccate su port filters e vi apparirà questo..

| Port Filters |
| --- |
| Filtering Rules |
| Add TCP/UDP Filter | Add Raw IP Filter | Return |

| Filtering Table |
| --- |
| Type | Start Port | End Port | Inbound | Outbound |  |  |
| TCP | 80 | 80 | Allow | Allow | Edit | Delete |
| UDP | 53 | 53 | Block | Allow | Edit | Delete |
| TCP | 53 | 53 | Block | Allow | Edit | Delete |
| TCP | 21 | 21 | Block | Allow | Edit | Delete |
| TCP | 23 | 23 | Block | Allow | Edit | Delete |
| TCP | 25 | 25 | Block | Allow | Edit | Delete |
| TCP | 110 | 110 | Block | Allow | Edit | Delete |
| TCP | 119 | 119 | Block | Allow | Edit | Delete |
| UDP | 7070 | 7070 | Allow | Allow | Edit | Delete |
| ICMP | N/A | N/A | Block | Allow | Edit | Delete |
| TCP | 1720 | 1720 | Block | Allow | Edit | Delete |
| TCP | 1503 | 1503 | Block | Allow | Edit | Delete |
| TCP | 22 | 22 | Block | Allow | Edit | Delete |
| UDP | 123 | 123 | Block | Allow | Edit | Delete |
| TCP | 443 | 443 | Block | Allow | Edit | Delete |
| TCP | 4661 | 4662 | Allow | Allow | Edit | Delete |
| UDP | 4671 | 4672 | Allow | Allow | Edit | Delete |
| TCP | 4241 | 4242 | Allow | Allow | Edit | Delete |

8 Cliccate su EDIT alla voce TCP 80 e impostate Allow su INBOUND e OUTBOUND

| Port Filters |
| --- |
| Edit Inizio modulo |
| Transport | Type | TCP |  |
| Port Range | Start Port |  |  |
|  | End Port |  |  |
| Direction | Inbound |  |  |
|  | Outbound |  |  |
| Return Fine modulo |

9 Cliccate su Apply…ritornete in questa schermata

| Port Filters |
| --- |
| Filtering Rules |
| Add TCP/UDP Filter | Add Raw IP Filter | Return |

| Filtering Table |
| --- |
| Type | Start Port | End Port | Inbound | Outbound |  |  |
| TCP | 80 | 80 | Allow | Allow | Edit | Delete |
| UDP | 53 | 53 | Block | Allow | Edit | Delete |
| TCP | 53 | 53 | Block | Allow | Edit | Delete |
| TCP | 21 | 21 | Block | Allow | Edit | Delete |
| TCP | 23 | 23 | Block | Allow | Edit | Delete |
| TCP | 25 | 25 | Block | Allow | Edit | Delete |
| TCP | 110 | 110 | Block | Allow | Edit | Delete |
| TCP | 119 | 119 | Block | Allow | Edit | Delete |
| UDP | 7070 | 7070 | Allow | Allow | Edit | Delete |
| ICMP | N/A | N/A | Block | Allow | Edit | Delete |
| TCP | 1720 | 1720 | Block | Allow | Edit | Delete |
| TCP | 1503 | 1503 | Block | Allow | Edit | Delete |
| TCP | 22 | 22 | Block | Allow | Edit | Delete |
| UDP | 123 | 123 | Block | Allow | Edit | Delete |
| TCP | 443 | 443 | Block | Allow | Edit | Delete |
| TCP | 4661 | 4662 | Allow | Allow | Edit | Delete |
| UDP | 4671 | 4672 | Allow | Allow | Edit | Delete |
| TCP | 4241 | 4242 | Allow | Allow | Edit | Delete |

10 A questo punto aggiungete le porte che il firewall dovrebbe lasciarvi usare (questo in base ai server dove volete connettervi)… ad esempio se volete connettervi con Razorback2 seguite qusta procedura..

11 Cliccate su Add TCP/UDP Filter come nella figura sotto..

| Port Filters |
| --- |
| Filtering Rules |
| Add TCP/UDP Filter | Add Raw IP Filter | Return |

| Filtering Table |
| --- |
| Type | Start Port | End Port | Inbound | Outbound |  |  |
| TCP | 80 | 80 | Allow | Allow | Edit | Delete |
| UDP | 53 | 53 | Block | Allow | Edit | Delete |
| TCP | 53 | 53 | Block | Allow | Edit | Delete |
| TCP | 21 | 21 | Block | Allow | Edit | Delete |
| TCP | 23 | 23 | Block | Allow | Edit | Delete |
| TCP | 25 | 25 | Block | Allow | Edit | Delete |
| TCP | 110 | 110 | Block | Allow | Edit | Delete |
| TCP | 119 | 119 | Block | Allow | Edit | Delete |
| UDP | 7070 | 7070 | Allow | Allow | Edit | Delete |
| ICMP | N/A | N/A | Block | Allow | Edit | Delete |
| TCP | 1720 | 1720 | Block | Allow | Edit | Delete |
| TCP | 1503 | 1503 | Block | Allow | Edit | Delete |
| TCP | 22 | 22 | Block | Allow | Edit | Delete |
| UDP | 123 | 123 | Block | Allow | Edit | Delete |
| TCP | 443 | 443 | Block | Allow | Edit | Delete |
| TCP | 4661 | 4662 | Allow | Allow | Edit | Delete |
| UDP | 4671 | 4672 | Allow | Allow | Edit | Delete |
| TCP | 4241 | 4242 | Allow | Allow | Edit | Delete |

12 Vi troverete qua..

| Port Filters |
| --- |
| Add TCP/UDP Filter Inizio modulo |
| Transport | Type |  |  |
| Port Range | Start Port |  |
|  | End Port |  |
| Direction | Inbound |  |
|  | Outbound |  |
| Return Fine modulo |

13 Su transoprt Type selezionate TCP.. su Port Range alla voce Start port mettete 4661

E alla voce End port mettete 4662

14 Alla voce Direction lasciate Allow su entrambe

15 Cliccate su Apply.

| Port Filters |
| --- |
| Add TCP/UDP Filter Inizio modulo |
| Transport | Type |  |  |
| Port Range | Start Port |  |
|  | End Port |  |
| Direction | Inbound |  |
|  | Outbound |  |
| Return Fine modulo |

16 Ora abilitate anche questa….

17 Su transport Type Selezionate UDP

18 Su start port mettete 4671 e su End port mettete 4672

19 Lasciate Allow su entrambe

20 Cliccate su Apply

21 A questo punto il procedimento è uguale su qualsiasi server vogliate connettervi, basta guardare la porta che usa il server .

Un consiglio. In start port mettete la porta più bassa di un numero, e in End port mettete la porta giusta. (potrebbe funzionare anche se i numeri delle porte sono uguali….ma no l’ho provato quindi non lo so)

22 Finita questa procedura cliccate su Save config to Flash

Status

Quick Start

Configuration

LAN

WAN

System

Firewall

General Settings

Packet Filter

Intrusion Detection

MAC Address Filter

URL Filter

Firewall Log

VPN

QoS

Virtual Server

Advanced

Save Config to FLASH

Language

E poi cliccate su Apply

Save Config to FLASH

Please confirm that you wish to save the configuration. Inizio modulo

There will be a delay while saving as configuration information is written to FLASH chips.

Fine modulo

A qusto punto dovreste poter usare Emule come volete…

Buon Divertimento.

P.S. Spero di essere stato chiaro anche in questo procedimento. Altrimenti sapete come contattarmi.

Alla Prossima  ……………….SKYZZO